## Slide 1: Proposed AX.25 Packet Network System
Josef Matondang

## Slide 2: AX.25 Packet Network Hardware Block Diagram

## Slide 3: AX.25 Packet Network Hardware Selection
Half-Duplex FM Radio AX.25 Network
  Wide-Band FM VHF Transceiver
  KISS TNC
  Antenna (Omnidirectional)
  Raspberry Pi Rev. 3
  Power Supply for Radio
Full-Duplex FM Radio AX.25 Network
  Analog Repeater
  Wide-Band FM VHF Transceiver
  KISS TNC
  Antenna (Omnidirectional)
  Raspberry Pi Rev. 3
  Power Supply for Radio
Half-Duplex LoRa AX.25 Network
  LoRa Module (SX1278)
  KISS TNC, Arduino based
  Antenna (Omnidirectional)
  Raspberry Pi Rev.3
  Power Supply for LoRa

## Slide 4: Half Duplex - FM VHF Transceiver Based

## Slide 5: FM Transceiver Based AX.25 Network: Radio
Radio: FC-302/D
Specification:
  FM Wideband 5W Power
  CTCSS/DTCS
  Max frequency deviation = 5 kHz
  Duplex
Connectors:
  Input: DB-15 Connector to Modem
  Output: Antenna via RG-58 BNC

## Slide 6: FM Transceiver Based AX.25 Network: Radio
Radio Alternative: Dorji DRA818V
Specification:
  FM Narrow-band 1W Power on 3.3V Power
  CTCSS/DTCS
  Max frequency deviation = 2.5 kHz
Board:
  Components:
    Level Translator (TTL5V – CMOS3V3)
    Power Amplifier (1W – 5W)
  Connectors:
    Input: Molex Conector for TTL and Power
    Output: SMA Connector Male for Antenna

## Slide 7: FM Transceiver Based AX.25 Network: KISS TNC
TNC: Mobilinkd
Specification:
  Serial KISS Mode with CSMA
  AFSK 1200 baud with HDLC
Board:
  Components:
    AF Impedance Matching (opt.) and AF Filters, ATmega328p + Arduino System Minimum.
  Connectors:
    Input: Serial Connector (USB) / Direct Serial Port to Raspberry Pi with Level Translator
    Output: Molex connector for Audio Out, Audio In; Molex Connector for Power

## Slide 8: FM Transceiver Based AX.25 Network: Antenna
Omnidirectional Antenna (2dBi) To avoid Hidden Transmitter Syndrome
Quarter Wavelength Whip Antenna (Nagoya NA-701)
Length: 21 cm
Connectors:
  BNC Connector

## Slide 9: FM Transceiver Based AX.25 Network: Raspberry Pi
Software:
  Client Socket Software
  Digipeater Socket Software
  Server Socket Software
Specification:
  Bluetooth + WiFi + USB Interface
Connections:
  Power via Micro USB

## Slide 10: Full Duplex – FM VHF Transceiver Based

## Slide 11: FM Transceiver Based AX.25 Network: Radio
Radio: FC-302/D
Specification:
  FM Wideband 5W Power
  CTCSS/DTCS
  Max frequency deviation = 5 kHz
  Duplex
Connectors:
  Input: DB-15 Connector to Modem
  Output: Antenna via RG-58 BNC

## Slide 12: FM Transceiver Based AX.25 Network: KISS TNC
TNC: Mobilinkd
Specification:
  Serial KISS Mode with CSMA
  AFSK 1200 baud with HDLC
Board:
  Components:
    AF Impedance Matching (opt.) and AF Filters, ATmega328p + Arduino System Minimum.
  Connectors:
    Input: Serial Connector (USB) / Direct Serial Port to Raspberry Pi with Level Translator
    Output: Molex connector for Audio Out, Audio In; Molex Connector for Power

## Slide 13: FM Transceiver Based AX.25 Network: Raspberry Pi
Software:
  Client Socket Software
  Digipeater Socket Software
  Server Socket Software
Specification:
  Bluetooth + WiFi + USB Interface
Connections:
  Power via Micro USB

## Slide 14: FM Transceiver Based AX.25 Network: Antenna
Omnidirectional Antenna (2dBi) To avoid Hidden Transmitter Syndrome
Quarter Wavelength Whip Antenna (Nagoya NA-701)
Length: 21 cm
Connectors:
  BNC Connector

## Slide 15: Half Duplex – LoRa Based

## Slide 16: LoRa Based AX.25 Network: Radio
Radio: SX-1278
Specification:
  Half-duplex SPI comm. to Microcontroller
  LoRa Modulation
  Power = 10mW
  CAD mode, RF detect, CRC 256 bytes

## Slide 17: FM Transceiver Based AX.25 Network: KISS TNC
TNC: Develop Own TNC
Specification:
  KISS Mode with CSMA
  Uses LoRa modulation, with CAD, LoRa packet framing
Board:
  SX1278
  Antenna Connector (SMA Male)
  SPI Level Translator

## Slide 18: FM Transceiver Based AX.25 Network: Raspberry Pi
Software:
  Client Socket Software
  Digipeater Socket Software
  Server Socket Software
Specification:
  Bluetooth + WiFi + USB Interface
Connections:
  Power via Micro USB

## Slide 19: FM Transceiver Based AX.25 Network: Antenna
Omnidirectional Antenna (2dBi) To avoid Hidden Transmitter Syndrome
Quarter Wavelength Whip Antenna (Nagoya NA-701)
Length: 21 cm
Connectors:
  SMA Connector Female